AQUAPANEL® Cement Board Floor

#### Solid floor with dry floor with fill ≥ 20 cm

Specification examples

| Item | Quantity / ME | Description of service | Unit cost | Total cost |
| --- | --- | --- | --- | --- |
|  | m2 m2 m2 m2 m2 m2 m2 m2 | Prepare, clean solid floor for receiving a dry floor. In the case of floors without basements: Apply a moisture barrier in acc. with DIN 18195 made of ___________________________, which is guided approx. _________ cm high (up to further horizontal sealing in the walls). In the case of new concrete floors or above wet rooms: Lay polyethylene film (e.g. 0.2 mm) loosely with 50 cm overlap. AQUAPANEL® Levelling Fill, installation thickness ________ mm (over 60 mm), must be removed with a superelevation of 10% flat with the plane over gauges. Uneven areas, pipes or cables must be covered by at least 10 mm. Lay cover panels (e.g. soft timber fibres, mineral fibres, plasterboard in accordance with EN520; note material thickness for layer height), tight against one another, avoiding cross joints and shifted to the joints on the fill. Subsequently lay panels or chip panel strips in sections and mechanically compress the fill on top of this with a hand stamper or a surface vibrator. AQUAPANEL® Levelling Fill, installation thickness ________ mm (over 60 mm), must be removed with a superelevation of 10% flat with the plane over gauges. Uneven areas, pipes or cables must be covered by at least 10 mm. Lay cover panels (e.g. soft timber fibres, mineral fibres, plasterboard in accordance with EN520; note material thickness for layer height), tight against one another, avoiding cross joints and shifted to the joints on the fill. Subsequently lay panels or chip panel strips in sections and mechanically compress the fill on top of this with a hand stamper or a surface vibrator. Lay AQUAPANEL® Cement Board Floor, 22 mm, cement-bonded dry floor element with surrounding slot in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. Apply AQUAPANEL® Interior Primer in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. AQUAPANEL® levelling Fill, maximum or minimum requirement per cm. |  |  |