AQUAPANEL® Cement Board Floor

Timber joist floor with dry floor with fill thickness ( 60 mm

Specification examples

| Item | Quantity / ME | Description of service | Unit cost | Total cost |
| --- | --- | --- | --- | --- |
|  | m2 m2 m2 m2 m2 m2 m2 | Prepare batten floor for receiving a dry floor, remove any coatings present, rescrew loose battens, replace damaged ones. Depending on the requirements as drip protection, fit a layer _____________ (packing paper, glass fibre mat or the like) with 10 cm overlap. AQUAPANEL® Levelling Fill, installation thickness ________ mm (up to 60 mm), must be removed with a superelevation of 10% flat with the plane over gauges. Uneven areas, pipes or cables must be covered by at least 10 mm. Fit mineral fibre impact sound insulation panels 12 – 1 mm, installation in accordance with the installation specifications of the manufacturer, tight against one another, avoiding cross joints and shifted to the joints on the fill. Lay AQUAPANEL® Cement Board Floor, 22 mm, cement-bonded dry floor pavement element with surrounding slot, in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. Apply AQUAPANEL® Interior Primer - internally in accordance with the processing instructions of Knauf Aquapanel GmbH & Co. KG. AQUAPANEL® Levelling Fill, maximum or minimum requirement per cm. |  |  |